## Slide 1: IMPLEMENTATION OF DIGITAL TECHNOLOGIES IN ALUMINA REFINING: A PRODUCER EXPERIENCE
Vladimir Golubev
RUSAL Engineering & Research Center
Notes: Enter speaker notes here.

## Slide 2: About the Presenter
Vladimir Golubev, RUSAL Engineering & Research Center
  Head of Mathematical Modeling Department,
  PhD in metallurgy (2007),
  18 years of experience, author of 6 books and >50 scientific papers.
Areas of Interests: simulation of process systems, CFD, machine learning, automation in alumina production.
List of co-authors: Dmitriy Mayorov, Evgeniy Fomichev, Dmitriy Chistyakov, Iliya Blednykh
No conflict of interest to declare
E-mail: vladimir.golubev2@rusal.com
Notes: Enter speaker notes here.

## Slide 3: Purpose of Digital Technology Implementation
Productivity increase
Improvement of management and decision-making procedures
Reduction of production costs
Reduction of harmful emissions
Key figures for UC RUSAL for 2019:
7.86 million tons of alumina produced
3.76 million tons of aluminum produced
43 refineries operate on 5 continents
> 90% of energy comes from renewable sources
<4 tons of CO2 equivalent emissions per ton of Al
Notes: Enter speaker notes here.

## Slide 4: Digital Technologies in Simulation of Processes at Alumina Refineries
CFD
Equipment optimization using fluid dynamics
Traditional Digital twins
Simulation and optimization of alumina refineries
Machine learning
Statistical models and advanced control
Notes: Enter speaker notes here.

## Slide 5: Computational Fluid Dynamics
Gas / Liquid
Gas / Solids
Liquid / Solids
Boiling / Condensation
Erosion
Combustion
Multiphase flows and processes
prevail in alumina production
Notes: Enter speaker notes here.

## Slide 6: Thickening and Washing
Dynamic simulation
of an industrial thickener
Flocculation with FBRM control
Refinery | Slurry | Year | Result
UAZ | Bauxite residue | 2016 | Increasing capacity by 31%
AGK | Gray mud (belite) | 2018 | Reducing overflow solids by 30% Reducing flocculant dosage by 15%
BAZ | Soda slurry | 2020 | Reducing OF solids by 20%
Ewarton | Bauxite residue | 2020 | Increasing UF solids up by 27%
Industrial implementations
Notes: Enter speaker notes here.

## Slide 7: Agitation in Tanks
Mixing with gas absorption
Refinery | Equipment | Year | Result
UAZ | Sc extraction unit | 2017 | 99-100% CO2 absorption
BAZ | Bauxite slurry tank | 2019 | Reducing the cost of scale removing by 30%
UAZ | Precipitator | 2020 | Increasing useful volume by 3%
AGK | Feed tank | 2021 | Trials delayed
Industrial implementations
Mech. mixing and air injection
Mechanical mixing
Air mixing
Notes: Enter speaker notes here.

## Slide 8: Abrasive and Cavitation Wear
Initial design
New design
Refinery | Equipment | Year | Result
Ewarton | Indirect bauxite slurry preheater | 2020 | No signs of wear, Increasing caustic in digestion by 14 g/L
Industrial implementations
Notes: Enter speaker notes here.

## Slide 9
Incrustation of Heat Exchangers
Stagnant zone
Refinery | Equipment | Year | Result
BAZ | Slurry cooler in precipitation | 2021 | Trials are in progress
Industrial implementations
Study of velocity pattern in the slurry cooler
Pipe-in-pipe heat exchanger with airlift
Water
inlet
Slurry
outlet
Slurry
inlet
Slurry
outlet
Slurry
inlet
Water
outlet
Air

## Slide 10: Calcination & Sintering
Temperature in the Flash Calciner
Refinery | Equipment | Year | Result
AGK | Sintering rotary kiln | 2017 | Understanding changes in flame parameters when switching over from coal to brown coal
UAZ | Flash calciner | 2019 | Reducing fuel consumption by 2.4% (estimated)
Industrial implementations
Burnout degree for different types of coal in the sintering kiln
Notes: Enter speaker notes here.

## Slide 11: Traditional Digital Twins
Development goal:
the digital twin should respond to technology and equipment changes in the same way as a real facility
SysCAD was chosen by RUSAL as a platform for creating traditional digital twins
Way to achieve the goal:
Simulation of process systems
METSIM
UniSim
Pro/II
Notes: Enter speaker notes here.

## Slide 12: Development of a Digital Twin
Laboratory research
Data from SCADA / MES
Chemical data
Data Integration into code of Digital Twin
Hardware specifications
Notes: Enter speaker notes here.

## Slide 13: Digital Twin Applications
Sensitivity study | Determination of the enterprise's reaction to changes in any process indicator
Ongoing optimization | Search for the optimum in terms of cost, productivity when external conditions change and the internal constraints occur
Assessment of investment efficiency | Quantification of the effect on cost and productivity in ramp-up projects, release of new products, and local improvements
Business planning | Calculation of key process indicators for the next planning period
Refinery | Start | Side Effect in 2020, $/t Al2O3
UAZ | 2015 | 1.49
BAZ | 2017 | 0.77
AGK | 2020 | 1.10
Industrial implementations at Russian Refineries
Notes: Enter speaker notes here.

## Slide 14: Machine Learning
Development goal:
creation of advisors for operators to simplify decision making and establish optimal process control
Ways to achieve the goal:
phenomenological models, machine learning,
hybrid models
Python, C#:
Scikit Learn, TensorFlow, Keras,
Self-developed mathematical and Bayer process libraries
Notes: Enter speaker notes here.

## Slide 15: Traditional Model of Precipitation
Population Balance Model
with updated secondary nucleation and binary breakage equations (ICSOBA, 2020)
Model allows to explain and predict oscillations of PSD
but
preparation and execution of one calculation takes up to
2 hours of machine time
Results of 1.5-year prediction: PSD, Liquor productivity, Nucleation rate, Number of particles.
Actual -45 um, %
Predicted -45 um, %
Notes: Enter speaker notes here.

## Slide 16: Deep Learning Model of Precipitation
PrecipExpert – decision aid system for prediction of time-series in precipitation: hydrate PSD (all sizes) and liquor productivity
60-day forecast for the content of -45 µm seed (at this figure the average correlation coefficient is 0.93)
Deep Neural Network
2 layers of LSTM + 1 layer of MLP,
about 50 000 trainable parameters
The model allows making new predictions of PSD and liquor productivity every 100 msec
In early 2021 correlation coefficient increased to 0.95
Notes: Enter speaker notes here.

## Slide 17: Optimal Control of Precipitation
Process restrictions |  |  | Results of optimization |  | 
Liquor flow | Average solids, g/L | Productivity of refinery | Content of -45 um | Average Lk of Spent liquor | Chemical Yield, %
1336 | 758 | 90,3 | 28,6 | 0,29 | 50,5
Effect: |  |  | -6,0 |  | +3,3
Study of optimal regimes of overcoming the historical periods of too fine hydrate
Content of -45 um in PSD, %
Date
Historical
Optimal
Moment of forecasting
11th March 2016
Content of -45 um in PSD, %
Date
Moment of forecasting
22nd December 2017
Historical
Optimal
Process restrictions |  |  | Results of optimization |  | 
Liquor flow | Average solids, g/L | Productivity of refinery | Content of -45 um | Average Lk of Spent liquor | Chemical Yield, %
1712 | 711 | 117,9 | 21,7 | 0,29 | 51,4
Effect: |  |  | -12,1 |  | -1,2
Notes: Enter speaker notes here.

## Slide 18: Online Refinery Optimization
Absolute stability
Automatic solution
Constant calculation time
Smartphone or PC is enough
Computing time:
- one iteration – sec / msec
- optimal search – minutes
Deep Neural Network
Unstable solution
Manual control
Unpredictable calculation time
Cloud or cluster computing
Computing time:
- one iteration – hours
- optimal search – days or months
Traditional Digital Twin
Faster
Simpler
Cheaper
Notes: Enter speaker notes here.

## Slide 19: Next Generation of Digital Twins
Multivariable problems
Strict relations
Parametrical stability
Explainability
Traditional Digital Twins
Computational Fluid Dynamics
Design Dependency
Accurate & Complicity
Reproducibility
Scalability
Machine Learning
Unknown dependences
Probability estimation
Adaptivity
Quickness
Refinery
Data consistency
Data availability
Data completeness
Notes: Enter speaker notes here.

## Slide 20: Adjusted Metal Balance
Bauxite slurry
Digested Slurry. Solids
Digested Slurry. Liquor
Digestion
Spent liquor
Flow | Abs. error | Measured | Adjusted
Bauxite | 5 | 100 | 95
Spent liquor | 2 | 60 | 59
Slurry. Solids | 2 | -12 | -13
Slurry. Liquor | 3 | -140 | -141
Delta |  | 8 | 0
Material balance restriction
Optimization target
Al balance
Notes: Enter speaker notes here.

## Slide 21: Adjusted Measurements
improved measurement accuracy
elimination of redundancy of measurements
construction of smart sensor network
consistent balances of alumina, soda, impurities
sensors malfunction monitoring
Advantages
Conditions and restrictions:
Optimization target
mass balance
energy balance
and process knowledge, i.e. for precipitation:
Al
Digestion
Evaporation
Mud field
Precipitation
Calcination
Soda
Heat
CHPP
Notes: Enter speaker notes here.

## Slide 22: ML and Nonlinear Approximation
Principal of Approximation of PDE operator using a feedforward neural network
(https://pypi.org/project/fluidlearn/)
Reverse Autodiff
=0
Notes: Enter speaker notes here.

## Slide 23: Solution of ODE and PDE by PINN
Physics-Constrained Machine Learning for Two-Phase Flow Simulation Using Deep Learning-Based Closure Relation
Chih-Wei Chang , Nam Dinh, and Sacit M. Cetiner, 2017
Physics Informed Deep Learning (Part I): Data-driven Solutions of Nonlinear Partial Differential Equations
Maziar Raissi, Paris Perdikaris, and George Em Karniadakis, 2018
Physics-informed machine learning approach for augmenting turbulence models: A comprehensive framework
Jin-Long Wu, Heng Xiao, and Eric Paterson, 2018
A Comprehensive Physics-Informed Machine Learning Framework for Predictive Turbulence Modeling
Jian-Xun Wanga , Jinlong Wua , Julia Lingb , Gianluca Iaccarinoc , Heng Xiaoa, 2018
Physics-informed machine learning for inorganic scintillator discovery
G. Pilania, K. J. McClellan, C. R. Stanek, and B. P. Uberuaga, 2018
A Physics-Informed Machine Learning Approach for Solving Heat Transfer Equation in Advanced Manufacturing and Engineering Applications
Navid Zobeiry, Keith D. Humfeld, 2020
An energy-based error bound of physics-informed neural network solutions in elasticity
Mengwu Guoa, Ehsan Haghighat, 2020
Literature references:
Real-time prediction of 2D time dependent heat transfer in solid plate by PINN (Navid Zobeiry, Keith D. Humfeld, 2018)
Notes: Enter speaker notes here.

## Slide 24: Mixed Density Network
Combination of a deep neural network (DNN)
and a mixture of distributions
(Dr. Oliver Borchers. From data to business value: Data Science, 2019)
(P. Sountsov, C. Suter, J. Burnim, J.V. Dillon, TensorFlow Prob. team, 2019)
Mixture Density Networks
Christopher M. Bishop, 1994
Regression with Probabilistic Layers in TensorFlow Probability
P. Sountsov, C. Suter, J. Burnim, J.V. Dillon, and the TensorFlow Probability team, 2019
Explainable and physics-informed machine learning for optimizing process chains and product quality
M. J. Neuer, D. Sonnenschein, H. Krambeer, M. Wunde, N. Holzknecht, M. Feldges, 2020
Literature references:
High precision prediction of scales on a rolled steel surface
(M. J. Neuer, D. Sonnenschein, H. Krambeer, M. Wunde, N. Holzknecht, M. Feldges, 2020)
Notes: Enter speaker notes here.

## Slide 25: Physics-Informed Machine Learning in Industrial Processes
Hybrid model will be stable while using industrial data, fast, scalable, adaptive, and capable for improvement
Production balance systems are used at alumina refineries
Approximation of nonlinear equations by neural networks has already been worked out
Algorithms for solving ODE and PDE by PIMM are available
Mixture Density Network (MDN regression) has been developed
There are examples of successful utilization of physics-informed machine learning models in industrial applications
Known parameters & relations
Physics-informed NN
Noise & Disturbances
Probability calculations
Unknown unknowns
Machine Learning
+
+
Process Data
Consistent measurements
+
Available knowledge:
Notes: Enter speaker notes here.

## Slide 26
www.rusal.com/ https://allow.rusal.com/
Please contact us by e-mail: vladimir.golubev2@rusal.com